## Slide 1
P33. Design of Primary and Secondary Controllers in HVDC systems
Young Faculty Research Seed Grant Proposal Dr. Lokesh Kumar Dewangan
Presented by- Maloth Karthikeya
220002047
End-Semester Evaluation Maloth Karthikeya 1
Supervisor: Dr. Lokesh Kumar Dewangan
Assistant Professor
Co-supervisor: Dr. Sharad Kumar Singh
Assistant Professor
Department of Electrical Engineering, IIT Indore 21st November 2025
EE-493
B.TECH PROJECT
End-Semester Evaluation

## Slide 2: Outline
Introduction
HVDC systems
Control
Real life examples in India
Literature Review
Key points from explored references
Zhang Bei HVDC grid
Key words
Problem Statement and Motivation
Goals and Deliverables
Methodology
Grid Connected converter and its control modelling
4-Terminal system with Multi-level modular converter modelling
Results
Simulation results of Grid connected converter system from PSCAD and its MATLAB validation.
Simulation results of 4-Terminal HVDC system from PSCAD.
Conclusions and Future scope
Conclusion.
Research and future scope
End-Semester Evaluation Maloth Karthikeya 2

## Slide 3: Introduction
High Voltage Direct Current(HVDC) systems employ a hierarchical control structure to maintain stability and coordination across converter stations. Which includes,
HVDC systems?
Converters?
https://powerline.net.in/wp-content/uploads/2017/12/Pg-65-A.jpg
The control architecture ensures fast, local regulation of active and reactive power, and DC voltage to stabilize the system during disturbances.
They enhance both the dynamic response and overall reliability of HVDC networks.
Fig.2 HVDC Projects in India
Fig.1 HVDC system
End-Semester Evaluation Maloth Karthikeya 3

## Slide 4: Literature Review
  Hierarchical control, comprising primary and secondary levels—enhances reliability, coordination, and performance in both point-to-point and multi-terminal (MT-HVDC) systems.
  Early studies, like Yazdani and Iravani (2010), established foundational VSC control for DC voltage and grid synchronization.
  Later exploring research works advanced to Grid connected systems, MMC-based systems, multi-terminal configurations, voltage control schemes.
  Key words:
  Grid modelling
  Converter modelling
  Control Architecture of converter
    PLL(Phase-Locked loop)
    abc-dq transformation ,
    Outer loop : Active and Reactive power control
    Inner loop : Current control
https://figures.semanticscholar.org/1a6c11856e11eb58f1926cbf9bad2d270848466f/2-Figure1-1.png
Fig.3 Zhang Bei HVDC grid in China
End-Semester Evaluation Maloth Karthikeya 4

## Slide 5: Problem Statement and Motivation
Goal:
Design HVDC systems with 2-level Voltage source converter(VSC) and Modular multi-level converter(MMC) with proper control architecture.
Simulation in PSCAD and MATLAB validation of the HVDC systems.
Deliverables:
The project outcomes should make a contribution towards increasing the stability, efficiency, and flexibility of HVDC transmission networks in future sustainable power systems.
End-Semester Evaluation Maloth Karthikeya 5

## Slide 6: Methodology
Design of HVDC system, Grid connected converter which include 2-Level converter(Fig4).
Converter Modelling
  Fig. 2 shows details of VSC control at which is connected to a grid through filters and transformer along with its control.
  A PLL(Phase-Locked loop) is used to estimate frequency of the grid which is also used for decoupling control design. The reference and measured values are given to the controller to control power.
  The modulating signal in dq frame mdq is generated using current control. The mdq is converted into mabc using inverse Park transform and is given to the VSC.
Fig.4 Grid connected converter(HVDC system)
Fig.5 Total Control scheme of VSC
End-Semester Evaluation Maloth Karthikeya 6

## Slide 7: Methodology
Fig.6 Phase Locked loop
Fig.7 Active power control
Fig.8 Reactive power control
  The controller output provides the reference currents (idref, iqref) for the inner control loop.
Outer control loop
Phase-Locked loop
End-Semester Evaluation Maloth Karthikeya 7

## Slide 8: Methodology
Inner current control
  This control loop regulates the converter’s output current, enabling rapid and precise tracking so that the actual current closely follows the reference value. See Fig9.
Fig.9 Inner current control
End-Semester Evaluation Maloth Karthikeya 8

## Slide 9: Methodology
Load flow analysis
Decision of Control mode
(PQ or Vdc)
Fig.10 Primary and secondary control flow diagram
End-Semester Evaluation Maloth Karthikeya 9

## Slide 10: Methodology
Multi-terminal system with Modular multi-level converter(MMC)(Fig11).
Fig.11 Multi-terminal HVDC system
T1,2,3,4 are 4-MMCs in which 2 are in active reactive power control mode(PQ) and other two are in voltage control mode(VdcQ).
End-Semester Evaluation Maloth Karthikeya 10

## Slide 11: Methodology
Follows same control architecture except it has submodules instead of one gate bridge like in VSC.
Fig.13 Control Scheme of MMC
Fig.12 Structure of MMC
End-Semester Evaluation Maloth Karthikeya 11

## Slide 12: Results
In the PSCAD design of Grid Connected Converter, values of pref and qref are set to constant 1pu and 0pu up to 2-seconds then there is a step change of 1 to 1.5pu and 0 to 0.2pu from 2-seconds over simulation time, respectively.
See Fig.14 for power outputs at PCC. and Fig.15 below for the output waveforms of PCC currents id, iq and reference currents from active and reactive power control scheme idref, iqref follow each other.
Fig.14 PCC powers in PSCAD design
Fig.15 d-q currents and references
It is observed that Power outputs follow the inputs and actual currents accurately tracking reference currents.
End-Semester Evaluation Maloth Karthikeya 12

## Slide 13: Results
Small-signal model MATLAB and PSCAD validation of the HVDC system
  A small-signal linearized state-space model of the system is designed in MATLAB with the same parameters as in PSCAD design.
  The outputs of Filtered currents, Filtered voltages and Power integrators are validated.
Fig.16 Inputs of Pref and Qref
Fig.17 Power control integrators
Fig.18 Filtered currents
Fig.19 Filtered Voltages
It is observed that the results obtained from both the PSCAD
and MATLAB are accurately tracking each other.
This confirms that the both models are identical under specified parameters.
End-Semester Evaluation Maloth Karthikeya 13

## Slide 14: Results
Below are the MATLAB imported PSCAD simulation results of 4-terminal HVDC system.
Fig.20 Currents and reference currents in MMC1
Fig.21 Currents and reference currents in MMC3
Observe that the currents Iod,Ioq and reference currents Iodred,Ioqref follow each other in both the MMCs.
End-Semester Evaluation Maloth Karthikeya 14

## Slide 15: Conclusions and Future scope
Research and future scope
  There are many ideologies to develop from the design of HVDC systems.
  Operating behavior of HVDC system
  Interaction analysis involving HVDC converters and multi-terminal grids.
  Small-Signal (Linearized) Stability Analysis
  Frequency-domain stability analysis
  State-space modelling.
This project successfully designed and validated primary and secondary control structures for both VSC and MMC-based HVDC systems.
PSCAD simulations confirmed stable active/reactive power regulation, while MATLAB small signal model state-space models accurately matched the PSCAD responses.
The 4-terminal MMC-HVDC system demonstrated proper coordination between PQ-controlled and VdcQ-controlled terminals.
Overall, the work establishes a reliable modelling and control framework that improves the stability and flexibility of modern HVDC networks.
End-Semester Evaluation Maloth Karthikeya 15

## Slide 16: Appendix
Equations
Three 2-phase time invariant differential equations :
Three 3-phase time varying differential equations:
abc-dq transformation
Current control equations
End-Semester Evaluation Maloth Karthikeya 16

## Slide 17: Appendix
dvq_pll_dt = wf_PLL*(v_f(2) - vq_pll); % LPF the q-axis voltage
de_pll_dt = ki_pll*(0 - vq_pll); % PLL integrator
w_pll = kp_pll*(0 - vq_pll) + e_pll; % PLL frequency
dtheta_vsc_dt = wn*(w_pll - w); % Angular difference between frames
id_ref = kp_P*(p_ref - p_m) + e_P;
iq_ref = kp_Q*(q_ref - q_m) + e_Q; % Current references
de_CL_dt = ki_CL*(i_ref - i_f); % Integral action
vc_m = v_f + kp_CL*(i_ref - i_f) + e_CL + w_pll*l_f*Wpu*i_f; % PI + decoupling and FF
PLL
Power control loop
Current control loop
End-Semester Evaluation Maloth Karthikeya 17